## Slide 1
Pipeline Data Sheet – MC113
Salamander Solutions mineral insulated heater cables are manufactured using a continuous methodology, which enables long-length capability. Our patented manufacturing techniques produce mineral insulated cables which are unparalleled in performance, highly robust, and capable of delivering medium voltage power at long-lengths and high temperatures.
With continuous lengths of more than 2 km, external splicing can be minimized or eliminated altogether, greatly improving the reliability of the overall system. Internal transitions of the conductor allow for targeted heating in applications.
Each Salamander mineral insulated cable is designed and fabricated based on the heating requirements for the given application. A complete suite of high integrity cable and end connectors are available.
A
B
C
Conductor
Compressed MgO
Sheath
Pipeline and Subsea Applications:
  Pipeline Heating
  Molten Sulphur pipelines and transfer lines
  Bitumen / heavy oil lines
  High viscosity / waxy crude lines
  Subsea and Deepwater Flowline Heating
  Flow assurance: hydrate / wax prevention and mitigation
  Extended reach capability: access stranded reserves from existing hosts
Any long-length or high intensity heating requirements in challenging conditions.
Physical Data | 
Cable Diameter* | 1.13-inches (28.7 mm)
Sheath Material | Various Alloys
Conductor Material | CuNi Alloys
Insulation Material | Compressed MgO
Weight* | 3.70 kg/m
Min Bend Radius* | 1.0 meter
Pulling Tension* | 5 metric tons
Operating Data | 
Max Operating Voltage (L-L) | 11.4 kV*
Max Current | 300 A
Max Temperature (Continuous) | 650 °C (1200 °F)
Max Temperature (Intermittent) | 700 °C (1300 °F)
Min Storage Temperature | -65 °C (-85 °F)
Min Installation Temperature | -35 °C (-30 °F)
Internal
Conductor
Transition
05-2020
*single cable
*higher voltage rating than in-well application due to lower temperature operation

## Slide 2
In-Well Data Sheet – MC113
Salamander Solutions mineral insulated heater cables are manufactured using a continuous methodology, which enables long-length capability. Our patented manufacturing techniques produce mineral insulated cables which are unparalleled in performance, highly robust, and capable of delivering medium voltage power at long-lengths and high temperatures.
With continuous lengths of more than 2 km, external splicing can be minimized or eliminated altogether, greatly improving the reliability of the overall system. Internal transitions of the conductor allow for targeted heating in applications.
Each Salamander mineral insulated cable is designed and fabricated based on the heating requirements for the given application. A complete suite of high integrity cable and end connectors are available.
A
B
C
Conductor
Compressed MgO
Sheath
Applications:
  In-Well Heating
  Increases production in “cold flow” heavy oil wells
  Accelerates production and improves SAGD / CSS performance
  Provides flow assurance for waxy wells
  Enables in situ conversion of kerogen or in situ upgrading of heavy oil
Can address any long-length or high intensity heating requirements in challenging conditions.
Physical Data | 
Cable Diameter* | 1.13-inches (28.7 mm)
Sheath Material | Various Alloys
Conductor Material | CuNi Alloys
Insulation Material | Compressed MgO
Weight* | 3.70 kg/m
Min Bend Radius* | 1.0 meter
Pulling Tension* | 5 metric tons
Operating Data | 
Max Operating Voltage (L-L) | 8.66 kV
Max Current | 300 A
Max Temperature (Continuous) | 650 °C (1200 °F)
Max Temperature (Intermittent) | 700 °C (1300 °F)
Min Storage Temperature | -65 °C (-85 °F)
Min Installation Temperature | -35 °C (-30 °F)
Internal
Conductor
Transition
05-2020
*single cable